## Slide 1: Announcements
Lecture 3 updated on web. Slide 29 reversed dependent and independent sources.
Solution to PS1 on web today
PS2 due next Tuesday at 6pm
Midterm 1 Tuesday June18th 12:00-1:30pm. Location TBD.

## Slide 2: Review
Capacitors/Inductors
  Voltage/current relationship
  Stored Energy
1st Order Circuits
  RL / RC circuits
  Steady State / Transient response
  Natural / Step response

## Slide 3: Lecture #5
OUTLINE
Chap 4
  RC and RL Circuits with General Sources
    Particular and complementary solutions
    Time constant
  Second Order Circuits
    The differential equation
    Particular and complementary solutions
    The natural frequency and the damping ratio
Chap 5
  Types of Circuit Excitation
  Why Sinusoidal Excitation?
  Phasors
  Complex Impedances
Reading
Chap 4, Chap 5 (skip 5.7)

## Slide 4: First Order Circuits
KVL around the loop:
vr(t) + vc(t) = vs(t)
R
+
-
C
vs(t)
+
-
vc(t)
+
-
vr(t)
vL(t)
is(t)
R
L
+
-
KCL at the node:
ic(t)
iL(t)

## Slide 5: Complete Solution
Voltages and currents in a 1st order circuit satisfy a differential equation of the form
  f(t) is called the forcing function.
The complete solution is the sum of particular solution (forced response) and complementary solution (natural response).
  Particular solution satisfies the forcing function
  Complementary solution is used to satisfy the initial conditions.
  The initial conditions determine the value of K.
Homogeneous equation

## Slide 6: The Time Constant
The complementary solution for any 1st order circuit is
For an RC circuit,  = RC
For an RL circuit,  = L/R

## Slide 7: What Does Xc(t) Look Like?
 = 10-4
 is the amount of time necessary for an exponential to decay to 36.7% of its initial value.
-1/ is the initial slope of an exponential with an initial value of 1.

## Slide 8: The Particular Solution
The particular solution xp(t) is usually a weighted sum of f(t) and its first derivative.
If f(t) is constant, then xp(t) is constant.
If f(t) is sinusoidal, then xp(t) is sinusoidal.

## Slide 9: Example
KVL:
R = 5kΩ
+
-
C = 1uF
+
-
vc(t)
+
-
vr(t)
ic(t)
t = 0
vs(t) = 2sin(200t)

## Slide 10: 2nd Order Circuits
Any circuit with a single capacitor, a single inductor, an arbitrary number of sources, and an arbitrary number of resistors is a circuit of order 2.
Any voltage or current in such a circuit is the solution to a 2nd order differential equation.

## Slide 11: A 2nd Order RLC Circuit
R
+
-
C
vs(t)
i (t)
L
Application: Filters
  A bandpass filter such as the IF amp for the AM radio.
  A lowpass filter with a sharper cutoff than can be obtained with an RC circuit.

## Slide 12: The Differential Equation
KVL around the loop:
vr(t) + vc(t) + vl(t) = vs(t)
i (t)
R
+
-
C
vs(t)
+
-
vc(t)
+
-
vr(t)
L
+
-
vl(t)

## Slide 13: The Differential Equation
The voltage and current in a second order circuit is the solution to a differential equation of the following form:
Xp(t) is the particular solution (forced response) and Xc(t) is the complementary solution (natural response).

## Slide 14: The Particular Solution
The particular solution xp(t) is usually a weighted sum of f(t) and its first and second derivatives.
If f(t) is constant, then xp(t) is constant.
If f(t) is sinusoidal, then xp(t) is sinusoidal.

## Slide 15: The Complementary Solution
The complementary solution has the following form:
K is a constant determined by initial conditions.
s is a constant determined by the coefficients of the differential equation.

## Slide 16: Characteristic Equation
To find the complementary solution, we need to solve the characteristic equation:
The characteristic equation has two roots-call them s1 and s2.

## Slide 17: Damping Ratio and Natural Frequency
The damping ratio determines what type of solution we will get:
  Exponentially decreasing ( >1)
  Exponentially decreasing sinusoid ( < 1)
The natural frequency is 0
  It determines how fast sinusoids wiggle.
damping ratio

## Slide 18: Overdamped : Real Unequal Roots
If  > 1, s1 and s2 are real and not equal.

## Slide 19: Underdamped: Complex Roots
If  < 1, s1 and s2 are complex.
Define the following constants:

## Slide 20: Critically damped: Real Equal Roots
If  = 1, s1 and s2 are real and equal.

## Slide 21: Example
For the example, what are  and 0?
10
+
-
769pF
i (t)
159H

## Slide 22: Example
 = 0.011
0 = 2455000
Is this system over damped, under damped, or critically damped?
What will the current look like?

## Slide 23: Slightly Different Example
Increase the resistor to 1k
What are  and 0?
1k
+
-
769pF
vs(t)
i (t)
159H

 = 2455000

## Slide 24
Types of Circuit Excitation
Linear Time-
Invariant
Circuit
Steady-State Excitation
Linear Time-
Invariant
Circuit
OR
Linear Time-
Invariant
Circuit
Digital
Pulse
Source
Transient Excitations
Linear Time-
Invariant
Circuit
Sinusoidal (Single-
Frequency) Excitation
AC Steady-State
(DC Steady-State)
Step Excitation

## Slide 25: Why is Single-Frequency Excitation Important?
Some circuits are driven by a single-frequency sinusoidal source.
Some circuits are driven by sinusoidal sources whose frequency changes slowly over time.
You can express any periodic electrical signal as a sum of single-frequency sinusoids – so you can analyze the response of the (linear, time-invariant) circuit to each individual frequency component and then sum the responses to get the total response.
This is known as Fourier Transform and is tremendously important to all kinds of engineering disciplines!

## Slide 26
Representing a Square Wave as a Sum of Sinusoids
Square wave with 1-second period. (b) Fundamental component (dotted) with 1-second period, third-harmonic (solid black) with1/3-second period, and their sum (blue). (c) Sum of first ten components. (d) Spectrum with 20 terms.

## Slide 27: Steady-State Sinusoidal Analysis
Also known as AC steady-state
Any steady state voltage or current in a linear circuit with a sinusoidal source is a sinusoid.
  This is a consequence of the nature of particular solutions for sinusoidal forcing functions.
All AC steady state voltages and currents have the same frequency as the source.
In order to find a steady state voltage or current, all we need to know is its magnitude and its phase relative to the source
  We already know its frequency.
Usually, an AC steady state voltage or current is given by the particular solution to a differential equation.

## Slide 28: The Good News!
We do not have to find this differential equation from the circuit, nor do we have to solve it.
Instead, we use the concepts of phasors and complex impedances.
Phasors and complex impedances convert problems involving differential equations into circuit analysis problems.

## Slide 29: Phasors
A phasor is a complex number that represents the magnitude and phase of a sinusoidal voltage or current.
Remember, for AC steady state analysis, this is all we need to compute-we already know the frequency of any voltage or current.

## Slide 30: Complex Impedance
Complex impedance describes the relationship between the voltage across an element (expressed as a phasor) and the current through the element (expressed as a phasor).
Impedance is a complex number.
Impedance depends on frequency.
Phasors and complex impedance allow us to use Ohm’s law with complex numbers to compute current from voltage and voltage from current.

## Slide 31: Sinusoids
Amplitude: VM
Angular frequency:  = 2 f
  Radians/sec
Phase angle: 
Frequency: f = 1/T
  Unit: 1/sec or Hz
Period: T
  Time necessary to go through one cycle

## Slide 32: Phase
-8
-6
-4
2
4
6
8
-2
0
0
0.01
0.02
0.03
0.04
0.05
What is the amplitude, period, frequency, and radian frequency of this sinusoid?

## Slide 33: Phasors
A phasor is a complex number that represents the magnitude and phase of a sinusoid:
Time Domain
Frequency Domain